# PRESCRIBED BURNING PLAN

BURN PLAN #:  1-1-17

LANDOWNER NAME, ADDRESS, PHONE #:

Marcia Sheffield, (334) 315-6170

387 Pine Level Lane, Pine Level, AL, 36069

PLANNER NAME, CBM #, ADDRESS, PHONE #:

Hunter Johnson, AL #2124

3626 Lansdowne Drive, Montgomery, AL, 36111

(334) 303-3443

TRACT, STAND, LEGAL DESCRIPTION, COUNTY, LATTITUDE, LONGITUDE:

Sheffield Tract, Montgomery CO.

Longleaf Pine

32.07621 N° 86.06359 W°

LAST PBURN OR WILDLAND FIRE:  Not Since Planted

BURN ACREAGE: 120

EXPECTED MONTH OF BURN : December

ACREAGE BY RESOURCE OBJECTIVE:

SITE PREP (PLANT):

SITE PREP (SEEDING):

CUS:

##### TSI:  x

WILDLIFE HAB IMP: x

HZD FUEL REDUCTION: x

RANGE IMP:

BROWNSPOT:

OTHER (specify):

SPECIFIC OBJECTIVE(S):

Burn will improve timber stand, reduce grasses in stand, improve wildlife habitat

BURN UNIT DESCRIPTION (OVERSTORY/UNDERSTORY):  75% understory, 15% overstory

TOPOGRAPHY-ASPECT-SLOPE-SOILS: 0-30° W. aspect, sandy/sandy loam

FUEL MODEL(S) AND % AREA REPRESENTED OF BURN AREA:

FM-2 (75%), FM-3 (15%)

ADJOINING FUEL MODEL(S) OUTSIDE OF BURN UNIT:

FM-1, FM-9, FM-11

ESTIMATED FUEL LOADING IN BURN AREA (tons/acre):

FM-2 (2 t.p.a.), FM-3 (3 t.p.a.)

CONTROL LINES (chains) ~ 248 chains of roads and bladed dozer lines

ROADS:  x

## STREAMS:

WET LINE:

DISKED: x

GREEN FIELD EDGE:

BLADED DOZER:  x

HAND LINE:

RECENT BURN:

##### RESOURCE NEEDS ONSITE

DOZER  _x_  TRACTOR/DISC _x__  ATV SPRAYER ___ ATV TORCH  ___  HELI ___   DRIPTORCH _x_  BLOWER  _x_   CHAINSAW _x__  RAKES _x__  SMOKE SIGNS _x__   PERSONNEL _5+__   VFD ENGINE ___    BACKPACK H2O _x__  OTHER (specify) ___

SPECIAL PRECAUTIONS, ADJOINING CONCERNS:

PLANTATIONS <15’ ___   PUBLIC ROADS _x__  HOMES _x__  HAYFIELDS _x__  CHICKEN HOUSES ___  STRUCTURES __x_   POWER POLES/BOXES  ___  FENCES _x__  OTHER _____

SPECIAL CONSIDERATIONS:

Clear-cut along west/north edge, hayfield along SE corner, 231 major SSA

DAYTIME SMOKE SCREENING COMPLETED:

Yes

FIRING TECHNIQUE:  BACKING _x_  FLANKING __  STRIP-HEAD ___  HEAD __  RING__

FIRING METHODS:  HAND _x__  ATV __x_  HELI ___

DISTANCE SCREENED: __2__ MILES

SMOKE SENSITIVE AREAS (SHOW ON MAP):

View Map

POSSIBLE NIGHT TIME IMPACT AREA (SHOW ON MAP):   View Map

SSA MITIGATION, CONTINGENCIES:

- Will notify any and all neighbors 1 week prior to burn

- Will notify ALEA, Montgomery CO. Sheriff Department, local VFD 1 week prior to burning

- If winds shift from SE, E, NE, towards U.S. 231, we will notify the proper authorities to handle traffic. Information can be found in Contacts.

- If fire escapes into FM-11 area, or others, AFC and local VFD will be notified

Burn will begin at approximately 13:00 hours. Crew will assemble at meeting zone inside highway gate at 12:00 hours. Crew meeting will commence, burn plan will be covered. On-Site weather conditions will be checked before ignition. Firebreaks will all be checked before ignition. Checklist will be analyzed before ignition. Once checklist a go, ignitors will take their positions along the ignition lines and suppressors and other personnel will be in their assigned locations. A radio check will occur at 12:55 hours. Once all crews have checked in, a test fire will be lit at 13:00 hours. Once test fire behavior is analyzed, ignition along the backwind flanks will occur. Suppressors will monitor fire while ignitors light the flank. Igniting will cease at 15:30 hours (2:30 hours since first ignition). Fire will be allowed to burn until dark, when FM% will increase and fire will cease. Mop-Up will occur the following day, along with post-burn evaluation. Pictures will be taken and reports will be assessed. A safety meeting will occur directly after burn and the following day. Goals for resource objectives and safety objectives will be analyzed. After burn, night-time drains will be monitored for smoke issues later that night (especially if LVORI is above 6)

BURNING PERMIT #:  _________________

DATE/TIME AUTHORIZED:

#### PRESCRIPTION PARAMETERS (FIRE OBJECTIVES)

DESIRED                    Suggested Ranges (by AFC)

TEMP                                                                       40°F – 50°F                    60°F or below

RH                                                                             40% - 60%                    30%-55%

MIDFLAME WS/DIRECTION                            2-3 mph SE                   2-6 mph

1 HR FM                                                                   7% - 9%                        6-9%

10 HR FM                                                                 8% - 10%                      7-10%

DISPERSION INDEX                                              41-70                             41+

MIXING HEIGHT (MIN)                                       5,000 ft.                         1,650 ft. – 6,500 ft.

TRANSPORT WIND & DIRECTION                  10-15 mph SE              9-20 mph

KBDI (LOCAL ESTIMATION)                             100-300                         0-300

LVORI                                                                        1-8 	1-8

POI                                                                              40%	0%-60%

ROS                                                                             10-15 cph (660-1000 ft)    N/A

FL                                                                                3 feet                               N/A

ATM Stability                                                            B-C	 B-C

Sky Cover                                                                   Clr/Pt Cldy	 N/A

ONSITE WX OBS                                   TEST FIRE            OBS 1             OBS 2          OBS 3

DATE

TIME

MIDFLAME WS

1 HR FM

10 HR FM

##### TEMP

RH

FLAME LENGTH

SKY

DRYING POTENTIAL

HOURS SUN

% PPT

START FIRING

COMPLETE FIRING

RXBP PREPARED BY:  Hunter Johnson

DATE: 8/7/17

TIME: 9:16 pm (CST)

CBM#: AL 2124

CBM EXPIRATION DATE: 10/1/2022

### ATTACHMENTS:

Burn Map (each block), Pictures, Smoke Screen (Day/Night), Weather Forecast

### BURN MAP _x__

### SMOKE SCREENING TOPO MAP _x__

### PICTURES ___ (after burn)

WEATHER FORECAST _x_

##### ORGANIZATION _x__

##### CONTACTS TO MAKE:  (COUNTY AFC, 911 DISPATCH OFFICE, LOCAL VFD, HUNT LEASE GROUP, ADJACENT OCCUPIED HOMES, ETC)

- ALEA – (334) 274-0196

- AFC (334) 240-9300

- South Montgomery CO. Fire – (334) 562-9280

- Montgomery County Sheriff Dept. – (334) 832-4980

Weather Forecast Example. Day of Forecast will be taken and stapled to burn sheet once evaluated and recorded.

STATE OF ______________

COUNTY OF ______________

I, THE UNDERSIGNED AUTHORITY, A NOTARY PUBLIC IN SAID STATE, HEREBY CERTIFY

THAT THIS BURNING PLAN WAS SIGNED BY ___________________________________, A STATE OF ALABAMA CERTIFIED PRESCRIBED FIRE MANAGER (#2124), PRIOR TO THE EXECUTION AND IMPLEMENTATION OF THE PRESCRIBE BURN AS ACKNOWLEDGED BEFORE ME ON THIS DATE GIVEN UNDER MY HAND AND OFFICIAL SEAL.

NOTARY PUBLIC:

DATE:

MY COMMISSION EXPIRES: 10/1/2022

# POST BURN EVALUATION

DATE OF BURN:

DATE RESULTS EVALUATED:

EVALUATION BY:

OBJECTIVES MET?:

AMOUNT OF LITTER LEFT:

% CROWN SCORCH:   SAPLINGS ____   PULPWOOD _____    SAWTIMBER ____

SPOTTING:

FORECAST ACCURATE?:

SMOKE RELATED PROBLEMS?:

PUBLIC COMPLAINTS?:

ADVERSE EFFECTS?:

RESTORATION NEEDS?:

CONTROL PROBLEMS?:

NEED FOR FUTURE EVALUATION?:

REMARKS:

https://drive.google.com/open?id=1nono_Xhle_zzJIszBMS46oGQFEk&usp=sharing

Hold control and click the link above. This will give you an interactive map about block size, acreage, burn type, and resource goal for each individual block.

Ignition Plan. Back-Fire planned into SE wind.

Dotted Line signifies ignition execution

Slashed Line indicates blacklining. This will occur a few days before the burn to ensure containment. Each block will be burned at different rates. (Pink and North most block will be burned first as a test block to ensure safety)